# Safe Operating Procedure

| Tool | Electric Planer |
| --- | --- |

| Potential hazards and safety controls |
| --- |
| Hazard | Control |
| Eye injuries | Wear safety glasses while using or standing near the electric planer. |
| Hand and body injuries | Secure the material firmly before starting the planer. Make sure the cutters are rotating at full speed before they make contact with the job. Always keep both hands on the planer, well clear of the cutters at all times, and plane with an even motion. Maintain a comfortable stance to one side of the planer. |
| Back injuries | Use good lifting practices when handling timber. Avoid twisting your body, and move with your whole body when changing direction. |
| Noise | Wear hearing protection when using or standing near the planer. |

Pre-start checks

Check that: planer cutters are sharp, in good condition, and are adjusted to the required depth electrical lead and extension lead are in good condition, planer starts up and runs normally, without any unusual noises or vibrations.

Operational procedure

Secure the material to be planed so that it cannot move. Position feet to give a comfortable balance and rest the front of the base plate on the job. Start the planer and allow it to reach full speed before commencing the cut. Push the planer smoothly forward with an even motion, in the direction of the grain. Keep power lead clear of the planer path. At the end of each sweep along the material, lift the planer off the job keeping your finger on the trigger.

### Sign-off

| Name | Paul Mack | Signature | Paul Mack | Date | 3/3/11 |
| --- | --- | --- | --- | --- | --- |